Manual

ESD VACUUM CLEANER

# A-ESD-MVAC

Technical Specifications:

Size(mm) :350*350*565

Capacity: 35L

Voltage: 120V or 230V/50Hz-60Hz

Power: 1250W

Power Cord lenghts: 4m

Hose length: 1.5m

Vacuum level: 18Kpa

Noize level: 82dBA (measured 1m from the unit with background noise 40db)

Surface Resistivity : 10E5~10E6 Ohms throughout entire system

The ZeroCharge Series clean room vacuums come standard with:

- a true HEPA cartidge filter

- one bag for dry vacuuming

- 10" ESD safe hose

- 16" ESD safe rubber flexible gooseneck

- standard ESD safe utility brush (to clean large areas such as floors, raised floors, and tabletops)

- A sponge filter for wet vacuuming

The unit has built-in EMI/RFI filter  for safe use around electronic equipment.

Most frequent applications:

-Board handling areas

-Equipment assembly cleaning

-Clean rooms cleaning

WARNING: To reduce the risk of electric shock, this unit has a polarized plug (one blade is wider than aonther). This plug will fit in a polarized outlet only one way. If the plug does not fit fully in the outlet, reverse the plug. If it still does not fit, contact a qualified electrician to install the proper outlet. Do not change the plug by yourself.

Description of parts：

1、Handle  2、ON/OFF switch  3、Top section  4、Filter basket   5、Safety float valve  6、Clasp  7、Container  8、Vacuum hose connection  9、Rollers  10、Flexible vacuum hose  11、Plastic tube  12、Blow connection  13、Wet brush  14、Sponge Filter  15、Short nozzle  16、Pedestal  17、Clasp seat  18、Accessory holder  19、Paper dust bag  20、Square round brush  21、Water drain screw

22、HEPA Filter

●Attention: Before assembly and starting operation, read the operating instructions carefully.

●Check that the supply voltage to make sure that it corresponds to the voltage indicated on the  unit label.

●Only connect to a proper 220-240 volt, 50/60Hz socket

●Pull the mains plug out of the socket when: the unit is not in use, before opening the unit and before cleaning and maintenance.

●Never clean with solvents.

●Do not use the cable to pull the plug out of the socket.

●When unit is ready for use, do not leave unattended.

●Keep away from children.

●The unit must not be operated if the mains connection lead is not in perfect condition.

●On no account vacuum:  burning objects, glowing ashes and cigarette ends, inflammable, corrosive,   fire hazard or explosive substances, vapors and liquids.

●This unit is not suitable for vacuuming dust  which is damaging to health.

●Store the unit in a dry place.

●Do not operate a defected unit.

●Service only by an authorized electrician.

●Use only for operations for which the unit is intended.

●Take great care when cleaning stairs.

●Use only manufacturer's attachments and spare parts.

Overview of nozzles

Assembly

Please Note:

* Figure 1: When you assemble products, please don't plug into electricity

* Figure 6a: Use the supplied foamed plastic filter for Wet vacuum-cleaning

* Figure 6b: Use the supplied paper dust bag for Dry vacuum-cleaning

Wet vacuum –cleaning

Pull the supplied foamed plastic filter over the filter Basket(Figure 2) for wet vacuum-cleaning.

The dust bag included upon delivery is not suitable for wet vacuum-cleaning.

Dry vacuum-cleaning

Slip the dust bag onto the socket (figure 2) for dry vacuum-cleaning.

The dust bag is suitable only for dry vacuum-cleaning.

Blowing

Please note:

Figure 1: when you blowing the dust or ash, please connect the hose on blowing connection

Maintenance cleaning

Cleaning the tank:

After working or when the tank is full of dust/liquid, what significantly decreases the suction power, remove the plug from the electrical outlet and clean the drum. To do this, unhook the two locks and remove the suction unit and the filter. Remove the filter and clean the dust/liquid from the tank.

SMT: www.Assembly-SMT.com www.SMT-tool.com www.X-Reflow306.com, www.X-1003.com www.SMTrepair.com www.SMTFocus.com www.FineRework.com www.SMTdispenser.com www.BestBatchOven.com

ESD: www.ESDapparel.com www.ESDmeters.com www.ESDpackaging.net www.ZeroCharge.net www.No-Stat.com www.ESDchair.com www.ESDlabcoats.com www.ESDcarts.net www.ESDchair.com www.ESDbrushes.com

Other: www.SuperiorScrewdrivers.com www.Super-Iron.com Latest Additions: www.PCBprototypingRobot.com www.ECOguardCC.com www.ProportionAir.com , www.RRlotion.com www.ULT.de (The best fume extractors)

# Text boxes

P/N X-DOC173

Sep 08-2013

Rev. 2

| 650 Scranton Pocono Hwy Covington Twp., PA 18444, USA Tel: (570) 842-2812 Fax: (570) 842-4290 E-Mail: bokar@bokar.com www.bokar.com, www.SMTrework.net, www.SMT-tool.com, www.ESDmeters.com, www.SMTreballing.net, www.FineRework.com, www.X-Reflow306.com, www.ZeroCharge.net |  |
| --- | --- |